## Slide 1: Bridge Inspection Robot Proposal Presentation
Sean Csukas
Kristen Fernandez
Erikzzon Latoja
Justin Tamayo
Sanmeshkumar Udhayakumar
Advisor: Dr. Patricio Vela

## Slide 2: Introduction
The team designed a wireless sensing robot for structural health monitoring of steel structures
Replaced the old flexure-based, four-wheeled robot with a design that features upgraded electrical and mechanical components along with increased mobility
Previous Design by Dr. Wang’s Team
Current Design
Notes: Kristen

## Slide 3: Problem Background
The repair and maintenance of civil infrastructure systems is a constant challenge
  50+% of U.S. bridges built before 1940’s
  1 in 9 structurally deficient
  Maintenance costs ~$20.5 billion annually; only $12.8 billion available
  American Society of Civil Engineers (ASCE) gave C+ grade for bridge infrastructure in 2017 Report Card on America’s Infrastructure
Visual inspection subjective and leaves damage below surface undetectable
Notes: Kristen

## Slide 4: Solution: Structural Health Monitoring (SHM) System
Utilizes accelerometer and other sensor data
Current Solutions - Stationary sensors
  Cons
    Cable installation between sensors is high cost
    Hard and time consuming to place and maintain
    A lot of sensors needed
  Resensys Senspot Sensors
    For average-sized highway bridge, would need ~500 sensors * $20 = $10,000, not including installation costs
    Human installation required roughly every 20 years
Notes: Kristen

## Slide 5
Network of robots capable of synchronized, autonomous traversal and structural health measurement
Benefits
  Only small number of robots needed to cover whole bridge
  Low-cost and no installation
Challenges
  No similar existing solution
  Drastically more complex
New Solution: Network of Wireless, Sensing Robots

## Slide 6: Goals
Design and build one robot to compose the new network
The robot must be able to do the following:
  Horizontally and vertically traverse steel bridges
  Measure bridge vibrations at low frequencies
  Wirelessly transmit vibration data to a PC
  Lightweight for deployment and retrieval by drone
Notes: Kristen

## Slide 7: Outline
Robot Overview
Mobility Design
  Motor Choice and Implementation
  Magnets
Accelerometer Measurements
  Accelerometer Choice
  Data Filtering
  Accelerometer Deployment
Motion Tracking
Microcontroller
Wireless Data Transmission
Power
Robot Structure
Verification
Final Demonstration Results
Notes: Kristen

## Slide 8
Robot Overview
Notes: Kristen

## Slide 9
Robot Mobility
Notes: Sean

## Slide 10: Three-Wheeled Design
Two motorized wheels in the front and passive omni-wheel at the back
Permanent magnets
  Surround motorized wheels
  Adjacent rear omni-wheel
Notes: Sean

## Slide 11: Mobility Choice: Three-Wheeled Design
Pros
  Retains capabilities of old flexure-based design
  Turn in place capability
  Less weight and power consumption compared to original design
Cons
  Omni-wheel provides less stability
  Currently lacks ability to traverse 90° angle
  Potential Solution:
    Leverage Arm
    Motorize back wheel
Notes: Sean

## Slide 12: Motors - Pololu 25D Metal Gearmotor
Motor includes encoder with 1200 counts per revolution
Includes low power option at 12V
  Free-Run Speed: 55 rpm
  Free-Run Current: 100 mA
Provides high torque needed for vertical traversal
  Stall Torque: 115 oz∙in
  Stall Current: 1110 mA
Notes: Sean

## Slide 13: Motors - Implementation
Motors placed in line with length of robot in order to minimize width
  Two beveled gears used to transfer motion 90° to wheels
Encoders provide 1,200 counts per rotation of the wheel
  Travelling one meter returns 4000 counts per wheel
Magnets are placed along the surface of the wheel
  Keeps robot attached to bridge on any surface
Notes: Sean

## Slide 14: Magnets - B621 Grade N42 Neodymium Magnet
Material: NdFeB, Grade N42
Weight: 0.36 g/magnet
Dimensions: 3/8” x 1/8” x 1/16” thick
Holding Force: 1.15 lbs.
Initial magnet choice was too large and too strong
  Motors had trouble producing enough torque to overcome holding force
  Due to size, initial magnets surrounding the wheel circumference turned the wheel into a polygon
  Chosen magnet was half the width to form a more uniform circle
Notes: Justin

## Slide 15
Accelerometer
Notes: Erikzzon

## Slide 16: Accelerometer Design Choices
Parameters | Initial Accelerometer: Silicon Designs 2460-002 | Final Accelerometer: Analog Devices ADXL355
Acceleration range | ±2g | ±2.048 g
Frequency Range | 0-300Hz | 0-10,000Hz
Resolution: | 38 ng/bit (with 2000x gain) | 3.8ug/bit
Noise Specification: | 10 μg/√Hz (before signal conditioning and A/D) | 25 μg/√Hz
Operating Power: | 276 mW (without A/D) | 495 μW
Mass | 21 g (without cabling and A/D) | ~5 g
Notes: Erikzzon

## Slide 17: Reason for Accelerometer Change
Noise Floor Requirements relaxed upon further conversations
  MRDC Bridge very small in comparison to other bridges
  Higher sensitivity needed for small structures
Digital over Analog
  Initial trepidation due to unfamiliarity
  Much less noise than analog
    Controlled environment within one module
    I2C bus hard to create noise in
  Can easily change digital filter parameters
No PCB for signal conditioning module needed
  Faster prototyping
Notes: Erikzzon

## Slide 18: Accelerometer Deployment Method
Requirements
  Accelerometer shall mount directly onto bridge
  Accelerometer shall be flush with bridge to ensure accuracy of measurements
Design incorporated vertical motion w.r.t. the Bridge Inspection Robot frame
Notes: Erikzzon

## Slide 19: Linear Actuator - Actuonix L12 30mm Linear Actuator
Prepackaged solution
Very low mass
Potentiometer already available for control
Gear Ratio: 210:1
Max Force: 80 N
Stall Current @ 12V: 180 mA
Control: RC
Notes: Erikzzon

## Slide 20: Deployment
Feedback not useful for control
  210:1 Gear Ratio made Linear Actuator was able to lift robot up off of magnetized surface
  Solution was to set input value to match the accelerometer position to exactly level with the contact surface of the wheels.
Accelerometer deployed inverted along the z-axis
  Allowed for accelerometer on board to be directly in contact with measurement surface
  Z-Axis Data only needed to be multiplied by -1 in post-processing to resolve
Notes: Erikzzon

## Slide 21: Digital Filter Parameters Option
Digital Filtering through Matlab
  firceqrip() or firgr()
FIR Filter
  Linear phase delay
Notes: Sanmesh

## Slide 22
Motion Tracking
Notes: Sanmesh

## Slide 23: Motion Tracking Requirements
Assumptions
  Initial orientation is known
  Only straight path traversal is required for the most part, with turning used for path corrections
Requirements
  Need to go in a roughly straight path so robot won’t need to continuously correct path
  Need to be able to detect edges so robot won’t fall off
  Need to be able to identify locations of structural health measurements to around about 2m resolution fairly accurately as in experiment in thesis paper
Notes: Sanmesh

## Slide 24: Straight Path Traversal
Encoders alongside proportional control used to maintain straight path
  Drift likely minimized due to permanent magnets holding wheels and robot body to metal surface
  Potential drift still a concern
  No permanent reference point
Plans to implement gyroscope in design for future use
Notes: Sanmesh

## Slide 25: Edge Detection
IR Sensors
  Four IR sensors mounted close to wheels and near edge
  Verified that wheels will hit inclines such that sensors will not scrape against surfaces
IR
Notes: Sanmesh

## Slide 26: IR Sensor Implementation
Notes: Sanmesh

## Slide 27: Motion Tracking
Used encoder movement, combined with GPS for absolute position recalibration every 50m
  Further minimizes effect of encoder drift
  Not useful if on underside of bridge without clear line-of-sight of the sky
Incorporate gyroscope in a future robot iteration
Notes: Sanmesh

## Slide 28: GPS - Adafruit Ultimate GPS Breakout - 66 Channel MTK3339
Accuracy: 3 m radius
Update Frequency: 10 Hz
Sensitivity: 165 dBm
Power: 100 mW
Interface: UART
Other
  Ships with breakout board
  Built-in data-logging
  SMA connector to connect external antenna
Notes: Sanmesh

## Slide 29: Gyroscope – ST L3GD20H
X-, Y-, Z-axis data
Resolution: ±245/±500/±2000°/s with 16 bits
Accuracy: Zero Bias: ±25°/s
Power: 15 mW
Interface: SPI/I2C
Other: User-enabled integrated low-pass and high-pass filters; Temp sensor.
Notes: Sanmesh

## Slide 30
Data Storage
Notes: Justin

## Slide 31: SD Card – Sparkfun microSD Breakout
Connects SanDisk Class 4 16 GB microSD card to MSP432
  Capable of storing over 370 hours of accelerometer data at a sample rate of 1000 Hz
Interfaced via SPI
  R/W Speed: 1 MHz
Notes: Justin

## Slide 32
Wireless Communication
Notes: Justin

## Slide 33: Wireless Module - XBee S2C 802.15.4
Specifications
  Max outdoor range: 1200 m
  Throughput: up to 250 Kbps
  Interface: UART
  Current draw (typical): 28-33 mA
  Wireless Protocol: IEEE 802.15.4
    Switched from Digimesh
Communicates with PC through a Sparkfun XBee Explorer USB
Notes: Justin
Outperforms the wireless module of the previous robot in all aspects - range, throughput, current draw, etc.
We later learned that a point-to-multipoint protocol is more desirable for synchronized nodes, but Digimesh is a mesh protocol that does not guarantee that every node will receive commands at the same time.
Initially, we were going to interface with the XBee via SPI,but UART proved to be simpler.

## Slide 34
Power
Notes: Sean

## Slide 35: Power Requirements
Power requirements were mainly dependent on the following:
  Motors
  Wireless Communication
  Accelerometer
  Accelerometer Deployment
The robot was expected to run actively for at least one hour and one additional hour while stationary
The robot required a maximum voltage of 12V to accommodate the accelerometer and motors. Power conversion circuitry used to create lower voltages for other components
Notes: Sean

## Slide 36: Turnigy Lipo Pack
Minimum Capacity: 2200mAh (True 100% Capacity)
Configuration: 3S1P / 11.1v / 3Cell
Weight: 188g
Provides a high continuous current and long lifetime
Notes: Sean

## Slide 37
Robot Structure
Notes: Sean

## Slide 38: Structure
A holding structure is needed for battery and circuitry
Structure was rapidly prototyped using Inventor 2017 and 3D printing with the Senior Design Lab
Alternate Consideration
  Aluminum or acrylic sheets are used for a high strength support, designed in Inventor 2017 and machined at the invention studio.
Notes: Sean

## Slide 39: Printed Circuit Board (PCB)
Designed using the educational license of Autodesk EagleCAD
Single circuit board for power, data transmission, and motor control
Used for routing signals between subsystems
Implements modular design to allow detachment or replacement of major components
Notes: Sean

## Slide 40
Microcontroller
Notes: Justin

## Slide 41: Microcontroller – TI MSP432P401R
Specifications
  48 MHz ARM 32-bit CPU
  256 kB of flash memory
  64 kB SRAM
  14-bit ADC
  4 UART channels and 4 SPI channels
  Current draw (active mode, typical): 7.8 mA
Programmed via Code Composer Studio IDE
MSP432 Launchpad used for rapid prototyping
Notes: Compared to MCU of previous robot: 8 Hz 8-bit MCU, 128 kB flash, 4 kB SRAM, 10-bit ADC, 17 mA current
Justin

## Slide 42: Software
Written in C
TI-RTOS: a proprietary RTOS for TI MCUs
  Libraries for GPIO, ADC, UART, SPI, Timers, etc.
  Separate threads for different components
    Mutexes, semaphores, and barriers sync and coordinate actions
External libraries for motors and GPS ported from Arduino to MSP432
Notes: Justin

## Slide 43: Datalogging Program
A "sample" consists of an X-value, Y-value, and Z-value
Accelerometer provides sequential data in sets of 8 samples
Double buffer system on MSP432, each holding 1536 samples
  Accelerometer fills one buffer with data while SD card is filled with the other buffer's data
Notes: Justin

## Slide 44: Movement Program
While motors are running...
  Encoder counts are incremented/decremented via interrupts
  Running timer regulates proportional control on the motors
  IR sensors halt forward progress if edge detected
Motors stop when the desired encoder count (distance) is reached
Notes: Justin

## Slide 45: User Interface Program
Commands are sent through a serial port (XBee)
Accelerometer data is streamed back at 115200 baud
  Data can be piped to a MATLAB program for automatic plotting
Notes: Justin

## Slide 46: Design Verification
Characteristic | Specification
Magnet Holding Force | Holds robot static indefinitely
Operational Lifetime | Movement Operation Time ≥ 1 hour; Recording Operation ≥ 1 hour
Accelerometer Range and Accuracy | 0 – 50 Hz ± 0.5 Hz 50 Hz +/- 0.5 Hz
Robot Size | Greatest side length ≤ 0.25 m
Weight | Total mass ≤ 1 kg
Wireless Communication Distance | Able to send/receive data ≥ 800 m
Path Following | Shall not fall off edge in “sunny day” conditions
Notes: Erikzzon

## Slide 47: Dimension and Mass Properties
 | Required Specification | Actual Specification | Requirement Met?
Dimensions | <= 25cm by 25cm by 25cm | 24cm by 14cm by 20cm | YES
Weights | 1 kg | 1.084 kg (5-7% overshoot on scale) | No

## Slide 48: Test Event: Holding Force
Initially proposed test was to check if an individual magnet could maintain its position with mass attached to it for at least 2 minutes
On further discussion, a more representative test would be testing the fully built robot with some mass attached to it in multiple configurations
Requirement is verified if robot can maintain its own mass and position in varying positions
  Stretch goal is the robot being able to maintain its position with extra mass attached
Notes: Erikzzon

## Slide 49: Holding Force Results
Robot upside down: Maintained position for at least 2 minutes
Robot on vertical surface: Maintained position for at least 2 minutes
  Robot is more secure if front wheels are on top
  If back wheel is on top, increased likelihood of the robot will flip over
  If robot is sideways, increased likelihood of back wheel slipping
Notes: Erikzzon

## Slide 50: Test Event: Accelerometer Data Accuracy
Verification of the accelerometer data accuracy required usage of a shaker table
A vibration profile will be measured by mounting both a statically mounted accelerometer and the robot with its installed accelerometer on to the table
Notes: Erikzzon

## Slide 51: Accelerometer Data Accuracy Results
No official testing event has occurred yet
Based on examination of data while integrating accelerometer into robot design, confident in accelerometer functionality
  Data produced is along the appropriate axes
  Small perturbations distinct
Notes: Erikzzon

## Slide 52: Test Event: Battery Life
Battery life analysis will be divided into movement operation time and measurement operation time
Movement operation time will be measured by having the motors drive continuously on metal surface as if it were traversing a bridge
Measurement operation time will be measured by having the robot collect ambient vibration data
Requirements will be met if each lifetime surpasses one hour
Notes: Erikzzon

## Slide 53: Battery Life Results
Upon further discussion, the highest current draw would be during the robot movement as the motors are driven
  By verifying the movement battery life requirement, the measurement battery life requirement is also verified
The robot was set to spin wheels freely while attached to a multimeter
  0.25V for 1hr
  Not completely representative as there is higher current draw when wheels are under load and magnetized to metal surfaces
Notes: Erikzzon

## Slide 54: Test Event: Wireless Communication Distance
The robot shall send data at distances varying linearly from 500m to 1000m to a base computer
Communication distance is verified if it can accurately send data at least 800m away from the computer
Notes: Erikzzon

## Slide 55: Wireless Communication Distance Results
Initial test sent GPS data back to base computer along 10th Street to the north of Georgia Tech’s main campus
  GPS data gave out at approximately 500 m
  Concerns regarding the foliage and passing cars obfuscating the signal
Retest to take place at Piedmont Park
  More open space and clearer line-of-sight between robot and PC
Notes: Erikzzon

## Slide 56: Test Event: Final Demonstration
The robot will be placed on the MRDC bridge and be expected to traverse to one of the measurement locations in each configuration
At each configuration, the robot will take measurements at one location simultaneously with stationary sensors at the remaining locations and send the data to the base computer
Measurement accuracy will be further confirmed by striking the bridge with a hammer during measurements
Notes: Erikzzon

## Slide 57: Final Demonstration
The “bridge” has been brought to the presentation
The robot shall:
  Move along the “bridge”
  Stop after moving for four seconds
    Robot should not fall off
  Deploy the accelerometer
  Measure data
  Transmit data wirelessly to PC
    Data shall be plotted in MATLAB
  Repeat the above procedure in triplicate
Notes: Erikzzon

## Slide 58: Future Steps
Integrate gyroscope for complex path following
Create network of robots for full mobile sensing network
Modify robot for drone deployment and retrieval
Incorporate localization
Notes: Kristen

## Slide 59: Cost Analysis
Notes: Kristen

## Slide 60: Questions?

## Slide 62
Notes: Kristen

## Slide 63
Notes: Kristen

## Slide 64: Before Low pass with 0.5 attenuation
After Low pass with 0.5 attenuation