## Slide 1: Bridge Inspection Robot Proposal Presentation
Sean Csukas
Kristen Fernandez
Erikzzon Latoja
Justin Tamayo
Sanmeshkumar Udhayakumar
Advisor: Dr. Patricio Vela

## Slide 2: Introduction
The team will design a wireless sensing robot for structural health monitoring of steel structures
Replace the old flexure-based, four-wheeled robot with a design that features upgraded electrical and mechanical components along with increased mobility

## Slide 3: Goals and Stretch Goals
Goals
  Ability to horizontally and vertically traverse steel bridges
  Measure bridge vibrations at low frequencies
  Wirelessly transmit vibration data to a PC
  Holding weight strong enough for future module attachments
  Light enough for deployment and retrieval by drone
Stretch Goals
  Complex Path following

## Slide 4: Mobility: Legged Design with Joints
Two legs attached with joints to a rigid body
Electromagnets at the “feet”
Servos placed at the joints move robot through waddling action
Pros
  Can turn any angle in one movement
Cons
  Cannot traverse inclines or corners
  Feet will scrape floor during movement
  Requires more movement controls
  Mechanical complications

## Slide 5: Mobility: Legged Design without Joints
Two legs attached without joints to a rigid body
Electromagnets at the “feet”
Servos placed in the legs move robot through waddling action
Pros
  Can turn any angle in one movement
  Mechanically simplified
Cons
  Requires more movement controls
  Cannot traverse inclines or corners
  Feet will scrape floor during movement

## Slide 6: Mobility: Two-Wheeled Design
Rigid body between two wheels
Permanent magnets surround wheels
Pros
  Simple movement controls
  Fast traversal of linear paths
  More power efficient
  Able to climb inclines
  Rotate in place
Cons
  Body will not stay parallel to surface on inclines – requires additional system for accelerometer deployment
  Magnets will keep wheels stationary when motors are driven

## Slide 7: Mobility: Three-Wheeled Design
Two motorized wheels in the front and a passive caster wheel/ball bearing at the back
Permanent magnets surround motorized wheels
Permanent magnet placed above ball bearing or around caster wheel
Pros
  Retains pros of previous design
  Solves movement problem of two-wheeled design
Cons
  Third wheel or bearing is a more complex implementation

## Slide 8: Mobility: Four-Wheeled Design
Single rigid body with two motorized wheels in front and two motorized wheels in the back
Permanent magnets surround wheels
Pros
  Smaller form factor
  Stable
Cons
  Higher weight and power consumption from extra motors
  Wheel width must be thin enough to allow slippage during turning but thick enough for magnetic forces

## Slide 9: Mobility Choice: Three-Wheeled Design
Overcomes forward movement problem of two-wheeled design
Retains all the pros of the two-wheeled design
Less weight and power consumption compared to four-wheeled design

## Slide 10: Motion Requirements
For this design, weight and power consumption need to be minimalized
RPM can be relatively low since the robot does not need to traverse the bridge extremely fast
  A four inch wheel turning at 60RPM would travel ~20m per minute
Moderate to high torque will be needed for angles up to 90°
There are not major space constraints on the motor
One motor would be required for each driven wheel
Encoder would be required, either built-in or as a separate module

## Slide 11: Motor Options
Motor Name | Motor Type | Operating Voltage | Current Draw | Torque | Speed | Interface | Weight
Dynamixel Ax-12 | Servo | 9V-12V | 50mA/900mA | 15.3kg-cm | 59 RPM | Async Serial | 55g
Futaba S3003 | Servo | 4.8V-6V | 8mA/400mA | 4.2kg-cm | 52 RPM | Analog | 44.2g
Tower Pro MG995R | Servo | 4.8V-6V | 30mA/400mA | 10kg-cm | 62 RPM | Pulse | 55g
Micro Gear Box Motor | BDC | 12V | 110mA/800mA | 4kg-cm | 100RPM | PWM | 193g
Pololu 37D metal gearmotor | BDC | 6V 12V | 250mA/2.5A 300mA/5A | 9kg-cm 18kg-cm | 80RPM 40RPM | PWM | 205g
Pololu 25D metal gearmotor w/ encoder | BDC | 12V | 100mA/1.1A | 6kg-cm 8kg-cm … | 71RPM 55RPM … | PWM | 104g

## Slide 12: Motor Choice
The Pololu 25D metal gearmotor with encoder is our ideal motor
The motor comes with a large variety of gear reduction options providing outputs ranging from 0.144 kg-cm at 5600 RPM to 23kg-cm at 100 RPM
The motor also offers 3 power options, High, Medium and Low power at 12V

## Slide 13: Accelerometer: Silicon Designs 2460-002
3-Axis version of the original Model 2012-002
  Significant lateral vibrations noted alongside vertical vibrations on the MARC bridge during previous testing
Input Range: ± 2 g
Frequency Response: 0 – 300 Hz
Differential Sensitivity: 2000 mV/g
Input Voltage: 8 – 32 VDC
Operating Current: 19 – 27 mA DC
Mass (without cabling): 21 g

## Slide 14: Accelerometer Deployment Method
Requirements
  Accelerometer shall mount directly onto bridge
  Accelerometer shall be flush with bridge to ensure accuracy of measurements
Design must incorporate vertical motion w.r.t. the Bridge Inspection Robot frame

## Slide 15: Method 1: Rack & Pinion
Pros
  Low torque and power requirements
  Simple design concept
Cons
  No existing prepackaged solution
  Rack adds excess weight

## Slide 16: Method 2: Linear Actuator
Pros
  Store-bought plug-and-play piece
  Less mass than rotary actuator for rack & pinion method
Cons
  Expensive to purchase
  Vertically space consuming

## Slide 17: Method 3: Solenoid
Pros
  Fast actuation from robot to bridge and back
  Easy start and stop indications for data collection
Cons
  No holding force, may be difficult to ensure proper contact
  High power consumption
Actuator | Stroke | Input Voltage | Watts | Mass | Interface
Series S-20-90-H | 50.8 mm | 12.1V | 9W | 155g | DC

## Slide 18: Design Decision: Linear Actuator
Actuonix L12 30mm Linear Actuator
  Prepackaged solution
  Very low mass
  Potentiometer already available for control
May explore Rack & Pinion further if Mechanical Engineer joins team or if complications occur

## Slide 19: Accelerometer Signal Conditioning Module
Prior testing showed structural vibrations yielded peak amplitude of only 0.125 mV at a vibration amplitude of 0.001 m/s^2
  Susceptible to circuitry noise
  Difficult to digitize with standard A/D Conversion
Custom Signal Conditioning Module used in previous design
  Amplifies and conditions signal before A/D Conversion
  Receiving support from Dr. Wang for updating the current module to work with new accelerometer

## Slide 20: Motion Tracking Requirements
Assumptions
  Initial orientation is known
  Only straight path traversal is required for the most part, with turning used for path corrections
Requirements
  Need to go in a roughly straight path so robot won’t need to continuously correct path
  Need to be able to detect edges so robot won’t fall off
  Need to be able to identify locations of structural health measurements to around about 2m resolution fairly accurately as in experiment in thesis paper

## Slide 21: Requirement 1: Straight Path
Need to go in a roughly straight path so robot won’t need to continuously correct path (only yaw is considered)
Possible Solutions:
  Gyroscope
    Pros: Cheap, simple data
    Cons: No constant reference, just measures change of angle so error can accumulate
  Magnetometer (basically compass):
    Pros: Cheap, simple data, constant reference of earth magnetic field
    Cons: Magnetometer reference will be skewed by permanent magnets on wheels
  Encoders
    Pros: Cheap, simple data, probably not much drift due to permanent magnets holding the wheels well to the bridge, can be used for path correction by spinning one wheel more than other
    Cons: Still potential for drift and no constant reference

## Slide 22: Requirement 1: Straight Path Cont.
Proposed solution:
  Use Encoders on motor
Stretch Goal:
  Implement gyroscope as well
  Will buy gyroscope and make sure gyro data is at least accessible

## Slide 23: Requirement 2: Edge Detection
Need to be able to detect edges so robot won’t fall off
Possible Solutions
  IR Sensors
    Pros: Implemented before, simple output, cheap
    Cons: Color of bridge could affect edge detection capabilities (may need to adjust thresholds for an edge "hit" from bridge to bridge)
  Ultrasonic sensors
    Pros: Color no longer an issue
    Cons: Generally more expensive than IR Sensors, sound-absorbent material blinds the sensor

## Slide 24: Requirement 2: Edge Detection cont.
Proposed Solutions
  IR Sensors
    Four IR sensors mounted close to wheels and near edge
    Will verify that wheels will hit inclines so that sensors will not scrape against surfaces
IR

## Slide 25: Requirement 3: Motion Tracking
Need to be able to identify locations of structural health measurements to around about 2m resolution fairly accurately as in experiment in thesis paper
Possible Solutions
  Solely Encoders
    Pros: Already on robot for previous requirements so dual purpose
    Cons: Encoder measurements not absolute so drift over long range
  GPS
    Pros: Absolute reference of position, pretty accurate (2m resolution)
    Cons: Won’t work in regions with poor receptions and under the bridge
  Separately bought IMU
    Pros: Very accurate for small movements, can potentially localize, and all filtering and sensor data-fusion already done
    Cons: Not accurate over large distances, can be expensive
  Use existing accelerometer in conjunction with encoders and gyroscope
    Pros: Very accurate for small movements, save money and weight by using sensors already needed for robot
    Cons: Need to implement filtering, sensor data fusion, and movement interpolation ourselves

## Slide 26: Requirement 3: Motion Tracking Cont.
Proposed Solutions
  Implement Now: Use encoder movement, combined with GPS for absolute position recalibration every 2m
    Pros: Removes drift of encoder, when under bridge can rely purely on encoders
    Cons: Extra part
  Future: Incorporate accelerometer and Gyroscope for extra position verification, and discard GPS
    Pros: Less cost
    Cons: Harder to implement accurately

## Slide 27: Gyroscope
Name | # of axes | Price | Resolution | Accuracy | Power Draw | Interface | Other
SparkFun Triple-Axis Digital-Output Gyro Breakout - ITG-3200 | 3 | $24.95 | ± (2000°/sec)/(2^16) = ± .0305°/sec | Zero Bias: ± 40°/s | 23.4 mW | I2C | user-selectable internal low-pass filter bandwidth. Fast-Mode I2C (400kHz). Temp sensor. Optional external clock inputs of 32.768kHz or 19.2MHz to synchronize with system clock
ST L3GD20H | 3 | $3.42 | ±245/±500/±2000°/s with 16 bits | Zero Bias: ±25°/s | 15 mW | I2C/SPI | User enabled integrated low-pass and high-pass filters. Temp sensor.
SparkFun Tri-Axis Gyro Breakout - L3G4200D | 3 | $49.95 | ±250/±500/±2000°/s with 16 bits | Zero Bias: ±245/±500/±2000°/s | 21.96 mW | I2C/SPI | Integrated low- and high-pass filters with user-selectable bandwidth

## Slide 28: GPS
Name | Price | Accuracy | Update Frequency | Sensitivity | Power | Interface | Other
Adafruit Ultimate GPS Breakout - 66 Channel MTK3339 | $39.95 | 1.8 m | 10 Hz | 165 dBm | 100 mW | Serial Comuniation | Comes with breakout board. Has in-built data-logging. SMA connector to connect external antenna.
GPS Bee with Mini Embedded Antenna | $16.00 | 2.5 m | 4 Hz | 160dBm | 200 mW | UART, USB, DDC and SPI interfaces | SMA connector to connect external antenna.
Venus GPS with SMA Connector | $49.95 | 2.5 m | 20 Hz | 165dBm | 297 mW | UART, SPI | Internal flash for optional 75K point data logging. SMA connector to connect external antenna.

## Slide 29: Magnets
Electromagnet
  Example specifications
    20x15mm
    12VDC @ 0.25A
    Strength: 5.5 lb.
Permanent magnet (neodymium)
  Example specifications
    No power cost
    3/4" x 3/8" x 1/16"
    Strength: 3.86 lb.

## Slide 30: Microcontroller – TI MSP432P401R
Specifications
  48 MHz ARM 32-bit CPU
  256 kB of flash memory
  64 kB SRAM
  14-bit ADC
  Current draw (active mode, typical): 7.8 mA
Programmed via Code Composer Studio IDE
MSP432 Launchpad will be used for rapid prototyping
Surface-mounted MSP432 will be incorporated into final design
Notes: Compared to MCU of previous robot: 8 Hz 8-bit MCU, 128 kB flash, 4 kB SRAM, 10-bit ADC, 17 mA current draw
Kristen and Justin have previous experience using this MCU

## Slide 31: Wireless Module - XBee S2C DigiMesh 2.4
Specifications
  Max outdoor range: 1200 m
  Throughput: up to 250 Kbps
  Data payload per frame: up to 256 Kbps
  Interface: SPI
  Current draw (typical): 28-33 mA
  Wireless Protocol: Digimesh
Raw conditioned data will be sent to PC for post-processing
Notes: Outperforms the wireless module of the previous robot in all aspects - range, throughput, current draw, etc.

## Slide 32: Power Requirements
Power requirements will be mainly dependent on the following:
  Motors
  Wireless
  Accelerometer
  Acc Deployment
The robot is expected to run for at least one hour actively and an additional hour stationary
The robot will require a maximum voltage of 12V to accommodate the accelerometer and motors. Power conversion circuitry will be used to create lower voltages for other components

## Slide 33: Battery Options
Battery Type | Voltage Rating | Capacity | Recharge? | Weight | Vendor
Alkaline AA | 1.5V | 1000mAh | No | 23g | Duracell
Alkaline 9V | 9V | 500mAh | No | 45g | Duracell
Ni-Mh AA | 1.2V | 2600mAh | Yes | 26.5g | Tenergy
Ni-Mh AAA | 1.2V | 1000mAh | Yes | 13g | Tenergy
Ni-Mh 9V | 9V | 250mAh | Yes | 86g | Tenergy
NiCd AA | 1.2V | 1000mAh | Yes | 27g | Tenergy
Li-Ion | 3.7V | 3000mAh | Yes | 45g | EBL
Li-Ion | 9V | 600mAh | Yes | 30g | EBL
Lipo 3S | 11.1V | 2200mAh | Yes | 170g | Turnigy
Lipo 3S | 11.1V | 5000mAh | Yes | 489g | Turnigy

## Slide 34: Battery Choice
Ni-Mh AAA (10 in series) or Lipo 3S
The Lipo can provide a higher continuous current and doesn’t need several in series, but would need a special charger

## Slide 35: Structure
A holding structure will be needed for the battery and circuitry
It can be rapidly prototyped using Inventor 2017 and 3D printing with the Senior Design Lab
A chassis is needed to support the motors and previously mentioned holding structure. Aluminum or acrylic sheets will be cut for a high strength support. This can also be designed in Inventor 2017 and machined at the invention studio
Both of these tasks will likely require assistance from and mechanical engineer

## Slide 36: Circuit Design
The design will use a single circuit board for power, data transmission, and motor control
It will be designed in using the educational license of Autodesk Eagle
Printing will be completed professionally by one of the following:
  Advanced Circuits - $33, 2 layer board up to 4”x6”, 2 week turnaround
  OSH Park - $5/sq-in for three boards, 12 day turnaround
  Senior Design Lab– Potentially free, 10 day turnaround

## Slide 37: Verification – Holding Force
Holding force of magnets will be verified by measuring the amount of time a magnet can maintain its position in different configurations
Requirement is verified if magnets can maintain their position with a 1kg mass attached at various locations for at least 2 minutes

## Slide 38: Verification – Accelerometer Data Accuracy
Verification of the accelerometer data accuracy will require usage of a shaker table
A vibration profile will be measured by mounting both a statically mounted accelerometer and the robot with its installed accelerometer on to the table

## Slide 39: Verification – Battery Life
Battery life analysis will be divided into traversal lifetime and holding lifetime
Traversal lifetime will be measured by having the motors drive continuously on metal surface as if it were traversing a bridge until the battery runs out
Holding lifetime will be measured by having the robot collect ambient vibration data until the battery runs out
Requirements will be met if each lifetime surpasses one hour

## Slide 40: Verification – Wireless Communication Distance
The robot shall send data at distances varying linearly from 500m to 1000m to a base computer
Communication distance is verified if it can accurately send data at least 800m away from the computer

## Slide 41: Final Demonstration
The robot will be placed on the bridge located at the MRDC and be expected to traverse to one of the measurement locations in each configuration
At each configuration, the robot will take measurements at one location simultaneously with stationary sensors at the remaining locations and send the data to the base computer
Measurement accuracy will be further confirmed by striking the bridge with a hammer during measurements

## Slide 42: Cost Analysis

## Slide 45: QUESTIONS?